Lab Safety

PROTECT YOUR EYES. Wear safety glasses at all times.

Do not attempt to operate any machine until you have read directions, had instructions and understand the machine.

Do not put sharp objects in your pockets

Remove watches, rings, I.D. badge, jewelry, neckties, and loose-fitting clothes prior to running machine. Do not operate machines with your backpack on.

Keep hair away from moving parts. Tie your hair back if necessary.

Remove all loose items (wrenches, chuck keys, rags, etc.) from machine before starting.

Do not operate any machinery while under the influence of alcohol, drugs, or medication

NEVER use you hands to remove chips and debris.

STOP the spindle completely BEFORE you take measurements or making adjustments.

Never use a compressed air hose to remove chips or to clean your skin.

Keep your work area clean well lit and dry. Sweep up chips, dry up oil and keep clear of obstacles.

Never lean on your machine. Avoid pinch points. Never operate a machine while sitting down. Do not leave a manual machine while it is running.

Securely clamp and locate work piece. Use stop blocks where necessary. KEEP clamps clear of cutter path.

PREVENT cutter breakage. Use correct table feeds and spindle speed for the job. Reduce feed and speed if you notice unusual noise or vibration.

Use the correct tool for the job.

Never start the machine when the cutter is in contact with the work piece.

Keep flammable liquids and materials away from work area and hot chips. Dispose of used rags properly.

Find and read all MSDS in your work area.

Never breathe smoke, dust or fumes. Always work in a well-ventilated area. Do not use chemicals and aerosols without adequate venting.

Do not run or fool around in a lab area. In other words: NO HORSEPLAY.

This is a general list of procedures. You should always be on the look out for any SAFETY HAZARDS or unsafe conditions.